## Slide 1
Focal Plane1, irregular hexagons
approximately 19 x 12 deg, 65 x 45 cm.
Red stars mark locations used to set mirror apertures in CodeV.
C, 145 GHz
D, 174GHz
B, 58.3 GHz
A, 48.6 GHz
Scan direction
Bottom of Focal Plane
Top of Focal Plane

## Slide 2
Pixel | Bands (GHz) | Upper edge of upper band (GHz) | Irregular hex Number | Bolometers per wafer | Area behind 1 wafer (mm^2) | Area needed for TDM chips (mm^2)
A | 21, 30, 43 | 48.6 | 60 | 60 | 8100 | 240
B | 25, 36, 52 | 58.3 | 100 | 60 | 8100 | 240
C | 62, 90, 129 | 145 | 366 | 366 | 5700 | 1500
D | 75, 108, 155 | 174 | 510 | 990 | 5700 | 3960
E | 186, 268, 385 | 433 | 480 |  |  | 
F | 223, 321, 462 | 520 | 450 | 1350 | 1730 | 5400
G | 555 | 624 | 220 | 1000 | 1730 | 4000
H | 666 | 749 | 200 |  |  | 
I | 799 | 899 | 180 |  |  | 
Focal Plane, irregular hexagons
  Wire bonding or bump bonding chips on focal plane?
    Wire bonds have heritage and allow more flexibility.
      Limited to 1400 detectors per wafer 1700 detectors per hex wafer (bond pitch = 80 um)
    Bump bonds allow more density of connections per chip.
    If KIDs (or similar) are dominate tech in 5 years this point is moot.
  Volume needed for 100 mK readout components? 4K readout components?
    100 mK TDM requires 4 mm^2 per channel (Hannes)
    100 mK FDM requires LCs, about 50-80 mm^2 channel (from EBEX-IDS, LCs on silicon wafer)
    4K, both need SQUIDs

## Slide 3
Orienting Q/U pixels
Q/U pixel pairs should follow each along scan path.
This is 0th order. Not account for distortion by the optics.
Showing only a single wafer pair, but all pairs would be similar.
Case 1 is original layout
Case 2 is rotated by 30 deg.
Scan direction
Case 1
Case 2
Left side of focal plane
Right side of focal plane
Close Q/U pair
Far Q/U pair
Far Q/U pair
Close Q/U pair

## Slide 4
Readout for central wafers
sky
Coupling optics, probably feedhorns
Bump bonds to circuit board
Printed circuit boards
Flex cable
TDM chips
Total thickness of few cm
  More TDM chips at 100 mK are needed than fit in the area behind 1 detector wafer
  We need bump bonds on the back of a wafer to connect the number of bolos to readout