## Slide 1
PICO Noise Model
Karl Young, Roger O’Brient, Shaul Hanany,
Qi Wen, Xin Zhi Tan

## Slide 2
Assumptions and Methodology
Methodology: Calculate in-band power absorbed by the detector, Popt. From Popt calculate bolometer thermal conductance, then NEP by source, then total NET per detector.
Assumptions
  Throughput for detector = lambda ** 2
  Bolometers sensitive to single polarization
  Spillover is terminated on the stop
  Mirror emissivity 0.07% at all frequencies
    Consistent with Planck Measurements
  All incident power is unpolarized
  Gaussian beam emitted by detector has 1/e2 angle:
    Based on our assumed detector architecture
  Gaussian beam varies with frequency within a given pixel (multi-chroic pixels)
  Photon Bose noise factor = 1
  Bolometer temperature is transition temperature Tc
  Bolometer Tc is optimal for given Psat.
  Including correlated Bose photon noise when pixel size is smaller than PSF
  Readout assumes current electronics as achieved by ground-based instruments, extrapolated to space incident power levels.
  End-to-end efficiency is 0.7
  Tophat bands

## Slide 3
Inputs to the code, Open Dragone
Parameter | Value |  | 
Band (top hat, no out of band loads) | 21 bands, 21 GHz to 800 GHz |  | 
Edge taper of pixel beam on stop (center band of MCP) | 10 dB |  | 
Telescope aperture | 140 cm |  | 
F-number | 1.42 |  | 
Mission length, efficiency, sky fraction | 4 yrs, 95 %, full sky |  | 
Bolometer attributes (same for all optics cases) |  |  | 
Psat to Popt safety factor | 2.0 |  | 
T_bath | 100 mK |  | 
thermal power law index (n) | 2 |  | 
Bolometer normal resistance | 1.33 Ohms |  | 
Bolometer loopgain | 25 |  | 
Optical element properties | Reflection loss | Emissivity | Temperature (K)
Bolometer absorption efficiency | 0.3 | 0 | 0.1
Mirror (secondary) | 0 | 0.0007 | 4
Stop | 0 | 1 | 4
Mirror (primary) | 0 | 0.0007 | 40
CMB | 0 | 1 | 2.725
Updated to March 2018 values

## Slide 4
Noise equations
Readout calculated using Francios Aubin’s code with input from Matt Dobbs
Power spectral density from optical elements and CMB.
Factor depends on n, T_bath, T_c. Is 0.5 for optimized T_c.
2 is due to single polarization